Electro-Hydro-Pneumatic POWER PACK

Model PS446-04

- General Data

  - An electro-hydro-pneumatic power supply for Military Applications, for the operation/actuation of powerful systems such as: heavy mechanisms, armored doors/hatches, heavy covers, etc.

  - The Power Pack is an independent “stand-by” energy source.   This means that in normal mode, accumulated energy is stored in a hydro-pneumatic accumulator, and, at command, a significant amount of energy is released during a pre-set period of time.

  - The Power Pack has a unique reservoir design, allowing installation and operation in a variety of inclinations.

  - The Power Pack complies with the entire range of mineral and synthetic hydraulic fluids.

2.	Technical Data

2.1 	Electrical:

2.1.1	Operating Voltage	18÷32 VDC

2.1.2 	Operating Current (max)	12 Amp

2.1.3 Electrical Connector	MIL-C-38999-20WC13-35PN

2.2. 	Hydraulic:

2.2.1 Flow (max)	0.4 LPM

2.2.2	Pressure (max)	180 bar

2.2.3	Reservoir Capacity	300 cc

2.2.4	Hydraulic Fluid	MIL-PRF-46170, MIL-H-5606,

Others - per request

2.2.5	Output Ports 	G1/8”, 7/16” JIC

2.2.6 Per request, larger capacities are available

2.3 	Dimensions: 	310 mm L x 305 mm W x 110 mm H

2.4 	Weight: 	15 kg